## Slide 1: PA Compression Test Software Improvements for M/A-COM
Nick Lalic
VNA Software Developer
Cupertino, CA
September 25th, 2015

## Slide 2: PA Compression Test
Three logical parts:
  Measurement
  Plot generation (on VNA)
  Data to Memory (Hold)

## Slide 3: PA Compression Test
Measurement
  Sweep power vs frequency
  Stop at compression
  Accommodate gain expansion
  Accommodate pulsed power conditions

## Slide 4: PA Compression Test
Plot Generation
  Current plot mechanism

## Slide 5: PA Compression Test
Plot Generation
  Request: plots on VNA
  Question: Are these trace settings sufficient?
  Options:
  Y Parameter: Input/Output Reflection, Gain, Reverse Gain, Pin, Pout
  Y Format: dB, mag, deg, rad, VSWR, dBm
  X Parameter: vs Frequency, vs Power
  At: Maximum Gain, Compression, Specific Frequency, Specific Power

## Slide 6: PA Compression Test
Plot Generation:
  Write measurement results into two channels with segmented sweeps
    Channel 1: Maximum gain
    Channel 2: Compression
  Benefits of this approach:
    Confirm, re-measure results
    Use VNA data processing capability
    Data export options available
Pin = Max. Gain, Compression vs Frequency

## Slide 7: PA Compression Test
Plot Generation
  Option 1 – Keep current plot selection tool, but generate plots on VNA
  Option 2 – Create a separate tool to generate plots on VNA
    Application to save current plot setup, recall plots later
    M/A-COM-specific PA plot generation script

## Slide 8: PA Compression Test
All traces data -> memory (hold)
  Functionality already built into ZVA:

## Slide 9: PA Compression Test
Overall workflow
OR