## Slide 1: VNA Software Applications
Nick Lalic
VNA Software Developer
Rohde & Schwarz North America
March 7-11th, 2016

## Slide 2: PA Compression Test

## Slide 3: PA Compression Test
Case study: MACOM Boston, Massachusetts USA
Setup:
  Pulsed RF power
  Driver amplifier
Calibration
  One Path, Two port
  Question: How to power cal?
Input Power (Pin)
Output Power (Pout)
PA S(f, Pin)
Power Cal. Plane
Calibration Planes
Port1
Port2
Driver
VNA

## Slide 4: PA Compression Test
Standard Power cal of source, receiver on Port 1
Calculate compression from S21(f, Pin)
Problems:
  No “2D” source power cal (vs power, frequency)
  Driver amplifier will drift
Option 1 – Power cal
Input Power (Pin)
Output Power (Pout)
S(f, Pin)
Power Cal. Plane
Calibration Planes
Port1
Port2
Driver
VNA

## Slide 5: PA Compression Test
Standard Power cal of source, receiver on Port 1
Enable ALC
Calculate compression from S21(f, Pin)
Problems:
  ALC is slow
  ALC (often) too slow for pulsed RF
Option 2: ALC
Input Power (Pin)
Output Power (Pout)
S(f, Pin)
Power Cal, ALC Plane
Calibration Planes
Port1
Port2
Driver
VNA

## Slide 6: PA Compression Test
Standard Power cal of source, receiver on Port 1
Measure source power (a1) along with S-Parameters
Calculate compression from S21(f, a1)
Option 3: Use measured power
Input Power (Pin)
Output Power (Pout)
S(f, Pin)
Power Cal. Plane
Calibration Planes
Port1
Port2
Driver
VNA

## Slide 7: PA Compression Test
Options 1, 2 illustrated
Measure S21, plot vs theoretical power
Use power cal, ALC to force actual power to theoretical
Option 3: Use measured power
Pin
Gain

## Slide 8: PA Compression Test
Option 3 illustrated
Meassure [S] vs measured power
Plot vs measured power
Option 3: Use measured power
Pin
Gain

## Slide 9: PA Compression Test
MACOM Boston, Massachusettes USA
Input Power (Pin)
Output Power (Pout)
PA S(f, Pin)
S1
a1
b1
S2
a2
b2
Power Cal. Plane
Calibration Planes
Port1
Port2
Driver

## Slide 10: PA Compression Test
Settings
Setup
Reference Channel

## Slide 11: PA Compression Test
Traces

## Slide 12: PA Compression Test
Y:
  S11, S21, S12, S22
  AM-PM Conversion
  Pin
  Pout
X:
  Frequency
  Pin
  Pout
At:
  Compression
  Max. Gain
  Frequency value
  Power value
Trace Options

## Slide 13: PA Compression Test
Mini GUI
Run (Measure, Update Traces)
Export
Exit

## Slide 14: Applications
Applications work with all VNAs
For each application:
  Application Card (PDF)
  Installer (MSI)

## Slide 15: VNA Software Webpage
http://vna.rs-us.net
Mobile

## Slide 16: Contact
Please contact me with feedback or requests
      Nick Lalic VNA Software Developer
      Cupertino, CA
      +1 (424) 200-2846 nick.lalic@rsa.rohde-schwarz.com
      http://vna.rs-us.net